## Slide 1: System Requirements Definition
Module 3

## Slide 2: Outline
Inputs-Activities-Outputs of Process
Characteristics of Good Requirements
Rules for Writing Requirements Statements
Stakeholder Requirements to System Requirements
System Requirements to Sub System Requirements
  SW Requirements
  HW Requirements

## Slide 3: System Requirements Definition Process
The purpose of the System Requirements Definition process is to transform the stakeholder, user-oriented view of desired capabilities into a technical view of a solution that meets the operational needs of the user.
(INCOSE Systems Engineering Handbook, v4)

## Slide 4
Problem
Domain
Solution
Domain
Did we build the right system?
Did we build the system right?

## Slide 5: System Requirements
System requirements are all of the requirements at the system level that describe the functions which the system as a whole should fulfill to satisfy the stakeholder needs and requirements, and are expressed in an appropriate combination of textual statements, views, and non-functional requirements; the latter expressing the levels of safety, security, reliability, etc., that will be necessary.
System requirements play major roles in systems engineering:
Basis of system architecture and design activities
Basis of system integration and verification activities
Means of communication between the various technical staff that interact throughout the project
Every requirement carries a cost!

## Slide 6: Inputs-Activities-Outputs of Process

## Slide 7: IPO Diagram

## Slide 8: Major Activities
Define System Requirements
Analyze Integrity of System Requirements
Define Verification Criteria

## Slide 9: Major Artifacts
System Requirements Document
  System External Interface Requirements Document
System Requirements Justification Documents
System Requirements Traceability

## Slide 10: Characteristics of Good Requirements

## Slide 11: Characteristics of Good Requirements (Individual)
C1 – Necessary
C2 – Appropriate
C3 – Unambiguous
C4 – Complete
C5 – Singular
C6 – Feasible
C7 – Verifiable
C8 – Correct
C9 – Conforming
Source: INCOSE Guide to Writing Requirements

## Slide 12: C1 – Necessary
If the requirement is not included, a deficiency in the capability or characteristic will exist, which cannot be fulfilled by implementing other requirements
A requirement is NOT necessary if:
  The requirement can be removed and the remaining set will still result in the needs being satisfied
  The requirement cannot be traced back to a source, need, or parent requirement
  The author cannot communicate a valid reason (rationale) for the requirement

## Slide 13: C1 – Necessary Example
Unacceptable:
  SR98: When ice is detected, car shall inform the user
  SR101: When ice is detected, car shall show an ice icon in less than 0.5 seconds from its detection
Improved (Removed duplicate vague requirement)
  SR101: When ice is detected, car shall show an ice icon in less than 0.5 seconds from its detection

## Slide 14: C2 – Appropriate
The specific intent and amount of detail of the requirement is appropriate to the level of the entity to which it refers
  Level: of abstraction, organization, or system architecture (system, subsystem, or system elements)
A requirement stated at the wrong level for an entity is either not correct or may not be verifiable at that level

## Slide 15: C2 – Appropriate Example
Unacceptable:
  Example 1:
  SR110: The user shall be categorized either as trusted or Not_Trusted
  Example 2:
  SR201: Thermistor input ADC shall have resolution of 10 bit
Improved
  SR110: The Security_System shall categorize each user as either Trusted or Not_Trusted
  SR201: Temperature_Measurement_System shall detect temperature with 0.1 degree C resolution

## Slide 16: C3 – Unambiguous
Requirement statements must be stated such that the requirement can be interpreted in only one way by all the intended stakeholders.
Ambiguity leads to interpretations not intended by the author, leading to problems such as schedule slips, budget overruns, failure of the SOI to pass system validation, and not be accepted for its intended use.

## Slide 17: C3 – Unambiguous Example
Unacceptable:
  SR110: When the clutch is disengaged and/or the break is applied, the Engine_Management_System shall disengage the Speed_Control_System within xxx milliseconds
Improved (Cleared ambiguity for consistent interpretation as per intent)
  SR110: When the [clutch is disengaged] AND the [break is applied] , the Engine_Management_System shall disengage the Speed_Control_System within xxx milliseconds
  OR
  SR110: When the clutch is disengaged, the Engine_Management_System shall disengage the Speed_Control_System within xxx milliseconds
  SR111: When the break is applied , the Engine_Management_System shall disengage the Speed_Control_System within xxx milliseconds
  OR
  SR110:When EITHER [the Clutch is disengaged] OR[the Brake is applied] the Engine_Management_System shall disengage the Speed_Control_System within xxx milliseconds

## Slide 18: C4 – Complete
The requirement statement sufficiently describes the necessary capability, characteristic, constraint, or quality factor to meet the need, source, or parent requirement from which it was transformed without needing other information to understand the requirement.
Each requirement should be understood in its own right without having to understand a number of other requirements.
Baselined requirement statements should not contain To Be Defined (TBD), To Be Specified (TBS), or To Be Resolved (TBR) clauses.

## Slide 19: C4 – Complete Example
Unacceptable:
  SR110: The Thermal_Control_System shall monitor system temperature
  Or
  SR110:The Thermal_Control_System shall update the display of System temperature
Improved
  SR110: The Thermal_Control_System shall update the display of System temperature
  every 10 +/-1 second in degree Celsius with an accuracy of +/- 0.2 degree Celsius.

## Slide 20: C4 – Complete Example 2
Unacceptable:
  SR210: The Corporate_Website shall display Approved_Fonts
Improved (Corrected as per intent)
  SR210: : The Corporate_Website shall display information using Approved_Fonts defined in Display_Standards_XXX

## Slide 21: C5 – Singular
The requirement statement should state a single capability, characteristic, constraint, or quality factor.
A requirement with multiple thoughts is difficult to allocate and to trace to a parent or source.
A nonsingular requirement is not verifiable

## Slide 22: C5 – Singular Example
Unacceptable:
  SR110: The control system will close the inlet_valve until the temperature has reduced to
  85 degree C, when it will then reopen it in less than 1 second
Improved (Split in two requirements each with it’s own time constraint)
  SR110: : If the Water_Temperature in the boiler increases to greater than 85 degree C, the Control_Subsystem shall close the Inlet_Valve in less than 1 second
  SR111: When the Water_Temperature in the boiler reduces to less than equal to 85 degree C, the Control_Subsystem shall open the Inlet_Valve in less than 1 second

## Slide 23: C6 – Feasible
The requirement can be realized within entity constraints (e.g.: cost, schedule, technical, legal, ethical, safety) with acceptable risk.
An infeasible need or requirement cannot be satisfied because
  it breaks the laws of physics,
  it violates laws or regulations in an applicable jurisdiction,
  it conflicts with another requirement and cannot be concurrently satisfied, or
  it leads to excessive program risk because of technical immaturity or inadequate cost/schedule margin

## Slide 24: C6 – Feasible Example
Unacceptable:
  SR210: The periodicity of the Engine RPM CAN Signal shall be 0.01 ms.
Improved (clear the definition)
  SR210: The periodicity if the Engine RPM CAN Message shall be 5 ms.

## Slide 25: C7 – Verifiable
The requirement statement is structured and worded such that its realization can be verified to the approving authority’s satisfaction.
  Otherwise, there is no way to tell if it has been satisfied and that the obligation has been met.
A requirement may not to be verifiable if there is:
  no clear definition of the correct functional behavior, conditions, and states.
  lack of accuracy or feasibility in the ranges of acceptable performance.
  use of ambiguous terms.
  no feasibility of the requirement.
  Absolute

## Slide 26: C7 – Verifiable Example
Unacceptable:
  SR210: The Weapon_System shall not fail
Improved (clear the definition)
  SR210: The Weapon_System shall have availability of greater than or equal to 95%
  or
  SR210:: The Weapon_System shall have a Mean_Time_Between_Failures of xxxx hours

## Slide 27: C8 – Correct
The requirement statement must be an accurate representation of the need, source, or parent requirement from which it was transformed.
Correct implies “no errors” both from the perspective of the inclusion of incorrect information, the omission of required information, and avoidance of ambiguous wording.
Incorrect information can mean having the wrong values, functions, conditions, or other characteristics identified in the requirement.

## Slide 28: C8 – Correct Example
Unacceptable:
  SR210: The Corporate_Website shall display Approved_Fonts
Improved (Corrected as per intent)
  SR210: : The Corporate_Website shall display information using Approved_Fonts defined in Display_Standards_XXX

## Slide 29: C9 – Conforming
Requirements should conform to an approved standard pattern and style guide or standard for writing and managing needs and requirements.
When requirements within the same organization have the same look and feel, each requirement statement is easier to write, understand, and review.
The people responsible for writing the needs and requirements may need to conform to the customer’s processes and standards.

## Slide 30: Characteristics of Good Requirements (Set)
C10 – Complete
C11 – Consistent
C12 – Feasible
C13 – Comprehensible
C14 – Able to be validated
Source: INCOSE Guide to Writing Requirements

## Slide 31: C10 – Complete
The requirement set for a given SOI should stand alone such that it sufficiently describes the necessary capabilities, characteristics, functionality, performance, drivers, constraints, interactions, standards, regulations, and/or quality factors without requiring other sets of requirements
The goal is to clearly communicate the requirements for an SOI via a minimum set that are necessary and sufficient and no more
Completeness of the set of requirements can be facilitated through the use of templates

## Slide 32: C11 – Consistent
The set of requirements contains individual requirements that are unique, do not conflict with or overlap with other requirements in the set
The units and measurement systems they use are homogeneous
The language used within the set of requirements is consistent
Consistency in requirements wording is greatly assisted using a centralized domain ontology, glossary, and data dictionary that is shared among all stakeholders.

## Slide 33: C12 – Feasible
Set of requirements can be realized within entity constraints (e.g., cost, schedule, technical) with acceptable risk.
The combination of feasible individual requirements does not necessarily imply a feasible set of those individual requirements
If feasibility is not addressed early in the development process, it can lead to wasted effort and cost.

## Slide 34: C13 – Comprehensible
The set of requirements must be written such that it is clear as to what is expected of the entity and its relation to the macro system of which it is a part.
This set must be written such that the relevant audience can understand what is being communicated
  An agreement is difficult to enact unless both parties are clear on the exact obligation and the expected outcome(s) as a result of the realization of the entity the set of requirements represents.

## Slide 35: C14 – Able to be Validated
It must be able to be validated that the set of requirements will lead to the achievement of the integrated set of needs and higher-level requirements within the constraints (such as cost, schedule, technical, and regulatory compliance) with acceptable risk.
Ask these questions:
  “Will the entity developed by this set of requirements satisfy the needs?”
  “Are we building the right thing?”

## Slide 36: Rules for Writing Requirement Statements

## Slide 37: Rules (1)
4.1 ACCURACY
  R1 - /Accuracy/SentenceStructure
  R2 - /Accuracy/UseActiveVoice
  R3 - /Accuracy/SubjectVerb
  R4 - /Accuracy/UseDefinedTerms
  R5 - /Accuracy/UseDefiniteArticles
  R6 - /Accuracy/Units
  R7 - /Accuracy/AvoidVagueTerms
  R8 - /Accuracy/NoEscapeClauses
  R9 - /Accuracy/NoOpenEnded
4.2 CONCISION
  R10 - /Concision/SuperfluousInfinitives
  R11 - /Concision/SeparateClauses
4.3 NON-AMBIGUITY
  R12 - /NonAmbiguity/CorrectGrammar
  R13 - /NonAmbiguity/CorrectSpelling
  R14 - /NonAmbiguity/CorrectPunctuation
  R15 - /NonAmbiguity/LogicalCondition
  R16 - /NonAmbiguity/AvoidNot
  R17 - /NonAmbiguity/Oblique
4.4 SINGULARITY
  R18 - /Singularity/SingleSentence
  R19 - /Singularity/AvoidCombinators
  R20 - /Singularity/AvoidPurpose
  R21 - /Singularity/AvoidParentheses
  R22 - /Singularity/Enumeration
  R23 - /Singularity/Context

## Slide 38: Rules (2)
4.5 COMPLETENESS
  R24 - /Completeness/AvoidPronouns
  R25 - /Completeness/UseOfHeadings
4.6 REALISM
  R26 - /Realism/AvoidAbsolutes
4.7 CONDITIONS
  R27 - /Conditions/Explicit
  R28 - /Conditions/ExplicitLists
4.8 UNIQUENESS
  R29 - /Uniqueness/Classify
  R30 - /Uniqueness/ExpressOnce
4.9 ABSTRACTION
  R31 - /Abstraction/SolutionFree
4.10 QUANTIFIERS
  R32 - /Quantifiers/Universals
4.11 TOLERANCE
  R33 - /Tolerance/ValueRange
4.12 QUANTIFICATION
  R34 - /Quantification/Measurable
  R35 - /Quantification/TemporalIndefinite
4.13 UNIFORMITY OF LANGUAGE
  R36 - /UniformLanguage/UseConsistentTerms
  R37 - /UniformLanguage/DefineAcronyms
  R38 - /UniformLanguage/AvoidAbbreviations
  R39 - /UniformLanguage/StyleGuide
4.14 MODULARITY
  R40 - /Modularity/RelatedRequirements
  R41 - /Modularity/Structured

## Slide 39: Rules to Characteristics Mapping
Source: Guide for writing good requirements - Helder Castro

## Slide 40: Rules – Accuracy (1)
R1 - /Accuracy/SentenceStructure
  Basic structure: The <entity> shall <action verb> <object>
  Example: The water bottle shall hold 1 litre of water
R2 - /Accuracy/UseActiveVoice
  Unacceptable: The audio shall by played by the system
  Acceptable: The system shall play audio

## Slide 41: Rules – Accuracy (2)
R3 - /Accuracy/SubjectVerb
  Unacceptable: The User shall
  Acceptable: The <system> shall
  Unacceptable The car shall have legroom of…
  Acceptable The Rear_Passenger_Seat shall have Legroom of…

## Slide 42: Rules – Accuracy (3)
R4 - /Accuracy/UseDefinedTerms
  Unacceptable: The system shall display the current date
  Acceptable: The system shall display the Current_Date in DD/MM/YYYY format
R5 - /Accuracy/UseDefiniteArticles
  Unacceptable: The system shall provide a time display
  Acceptable: The system shall display the Current_Time

## Slide 43: Rules – Accuracy (4)
R6 - /Accuracy/Units
R7 - /Accuracy/AvoidVagueTerms
  Unacceptable The system shall … at a maximum ambient temperature of approximately 60 degrees
  Acceptable The system shall … in the temperature range of -10 degrees Celsius to +60 degrees Celsius

## Slide 44: Rules – Accuracy (5)
R8 - /Accuracy/No Escape Clauses
  Unacceptable: The system shall, as far as possible, conform to Clause a) of Standard ABC
  Acceptable: The system shall conform to Clause a) of Standard ABC
R9 - /Accuracy/NoOpenEnded
  Unacceptable: The display_unit shall display date, time, temperature, etc.
  Acceptable: The display unit shall display Current_Date The display unit shall display Current_Time The display unit shall display Current_Temperature

## Slide 45: Rules - Concision
R10 - /Concision/Superfluous Infinitives
  Unacceptable The system shall be designed to be able to…
  Acceptable The system shall…
R11 - /Concision/Separate Clauses

## Slide 46: Rules – Non-Ambiguity (1)
R12 - /NonAmbiguity/CorrectGrammar
R13 - /NonAmbiguity/CorrectSpelling
R14 - /NonAmbiguity/CorrectPunctuation
R15 - /NonAmbiguity/LogicalCondition
  Unacceptable: The system shall X and Y
  Acceptable: The system shall [X AND Y]

## Slide 47: Rules – Non-Ambiguity (2)
R16 - /NonAmbiguity/AvoidNot
R17 - /NonAmbiguity/Oblique
  Unacceptable The system shall X and/or Y
  Acceptable The system shall X The system shall Y

## Slide 48: Rules – Singularity (1)
R18 - /Singularity/SingleSentence
R19 - /Singularity/AvoidCombinators
R20 - /Singularity/AvoidPurpose
  Unacceptable: The system shall… because
  Acceptable: The system shall…
R21 - /Singularity/AvoidParentheses

## Slide 49: Rules – Singularity (2)
R22 - /Singularity/Enumeration
  Unacceptable: The system shall display performance information
  Acceptable: The system shall display parameter #1 The system shall display parameter #2
R23 - /Singularity/Context
  Unacceptable: The system shall… X while Y within Z when A
  Acceptable: The system shall… as specified in Diagram #1

## Slide 50: Rules - Completeness
R24 - /Completeness/AvoidPronouns
  Unacceptable: The system shall receive from the user, his inputs
  Acceptable: The system shall receive inputs from User
R25 - /Completeness/UseOfHeadings
  Unacceptable: 5 Airbag Requirements 5.1 The car shall deploy them within X seconds of impact
  Acceptable: The car shall deploy Airbags in less than X seconds after Impact

## Slide 51: Rules – Realism, Conditions
R26 - /Realism/AvoidAbsolutes
  Unacceptable: The system shall never…
  Acceptable: The system shall… greater than or equal to 95%
R27 - /Conditions/Explicit
  Unacceptable: When X happens, the power shall be turned off
  Acceptable: In the event of X, the system shall turn off power

## Slide 52: Rules - Conditions, Uniqueness
R28 - /Conditions/ExplicitLists
R29 - /Uniqueness/Classify
R30 - /Uniqueness/ExpressOnce
  Unacceptable: The system shall generate a report of financial transactions The system shall generate a Financial_Transaction_Report

## Slide 53: Rules – Abstraction, Quantifiers
R31 - /Abstraction/SolutionFree
R32 - /Quantifiers/Universals
  Unacceptable: The Operation_Logger shall record any (or all) warning messages
  Acceptable: The Operation_Logger shall record each Warning_Message.

## Slide 54: Rules – Tolerance, Quantification
R33 - /Tolerance/ValueRange
  Unacceptable: The system shall… at acceptable levels
  Acceptable: The system shall… within the range X to Y
R34 - /Quantification/Measurable
R35 - /Quantification/TemporalIndefinite
  Unacceptable: The system shall…. Immediately
  Acceptable The system shall…. Within X seconds of Event_A

## Slide 55: Rules – Uniformity of Language
R36 - /UniformLanguage/UseConsistentTerms
R37 - /UniformLanguage/DefineAcronyms
R38 - /UniformLanguage/AvoidAbbreviations
R39 - /UniformLanguage/StyleGuide

## Slide 56: Rules - Modularity
R40 - /Modularity/Related Requirements
R41 - /Modularity/Structured

## Slide 57: Stakeholder Requirements to System Requirements

## Slide 58: Needs to Requirements
Problem Domain
Solution Domain
What Stakeholders
EXPECT from the System
System
Requirements
What the System must
DO / FULFILL
Stakeholder
Needs
Stakeholder
Needs
Stakeholder
Needs
Stakeholder
Requirements

## Slide 59: System Requirements Classification
Functional Requirements
Performance Requirements
Usability Requirements
Interface Requirements
Operational Requirements
Modes and/or States Requirements
Adaptability Requirements
Physical Constraints
Design Constraints
Environmental Conditions
Logistical Requirements
Policies and Regulations
Cost and Schedule Constraints
Regulatory Requirements
Source: SEBoK

## Slide 60: System Requirements Classification
Types of System Requirement | Description
Usability Requirements | Define the quality of system use (e.g. measurable effectiveness, efficiency, and satisfaction criteria).
Interface Requirements | Define how the system is required to interact or to exchange material, energy, or information with external systems (external interface), or how system elements within the system, including human elements, interact with each other (internal interface). Interface requirements include physical connections (physical interfaces) with external systems or internal system elements supporting interactions or exchanges.
Operational Requirements | Define the operational conditions or properties that are required for the system to operate or exist. This type of requirement includes: human factors, ergonomics, availability, maintainability, reliability, and security.
Modes and/or States Requirements | Define the various operational modes of the system in use and events conducting to transitions of modes.
Adaptability Requirements | Define potential extension, growth, or scalability during the life of the system.
Physical Constraints | Define constraints on weight, volume, and dimension applicable to the system elements that compose the system.
Design Constraints | Define the limits on the options that are available to a designer of a solution by imposing immovable boundaries and limits (e.g., the system shall incorporate a legacy or provided system element, or certain data shall be maintained in an online repository).
Environmental Conditions | Define the environmental conditions to be encountered by the system in its different operational modes. This should address the natural environment (e.g. wind, rain, temperature, fauna, salt, dust, radiation, etc.), induced and/or self-induced environmental effects (e.g. motion, shock, noise, electromagnetism, thermal, etc.), and threats to societal environment (e.g. legal, political, economic, social, business, etc.).
Logistical Requirements | Define the logistical conditions needed by the continuous utilization of the system. These requirements include sustainment (provision of facilities, level support, support personnel, spare parts, training, technical documentation, etc.), packaging, handling, shipping, transportation.
Policies and Regulations | Define relevant and applicable organizational policies or regulatory requirements that could affect the operation or performance of the system (e.g. labor policies, reports to regulatory agency, health or safety criteria, etc.).
Cost and Schedule Constraints | Define, for example, the cost of a single exemplar of the system, the expected delivery date of the first exemplar, etc.
Source : SEBOK WIKI

## Slide 61: Interface Requirements
The interaction could be direct (actual connection between two systems or
Indirect (no direct connection but there is some design feature of a system that can affect a design feature of another system, e.g., induced environments or competition for a common resource).
INCOSE-TP-2021-002-01 | VERS/REV: 1.1 | May 2022

## Slide 62: What an Interface is not!
A general rule is that the word “interface” should not be used in a requirement statement either as a noun or a verb.
  As a noun, it implies the interface is a thing, which it is not - it is a boundary across which, or at, two systems interact.
  As a verb, it is ambiguous, in that often there are multiple interactions between systems across a single interface boundary.
It is a best practice to focus on individual interactions when writing interface requirements. This is important from both a system verification perspective and an allocation perspective.
INCOSE-TP-2021-002-01 | VERS/REV: 1.1 | May 2022

## Slide 63: Example of how not to write Interface Requirements
Incorrect Requirement | Explanation | System A Requirement | System B Requirement
The digital interface shall maintain full operational capability after two failures. | This requirement assumes the interface is a tangible thing with functionality - this is not true. | The digital system on the spacecraft side shall maintain operational capability by handling up to two failures in data exchange. | The digital system on the payload side shall maintain operational capability by handling up to two failures in data exchange.
The interfaces between the spacecraft and payload shall be designed to …. | This requirement is written in passive voice on the designers and also assumes the interfaces are things. The requirement should focus on accessibility of connectors, bolts, etc. | The spacecraft shall provide accessible connectors and bolts for attachment to the payload. | The payload shall provide accessible connectors and bolts for attachment to the spacecraft.
The interfaces between the spacecraft and payload shall have standard labels, controls, and displays. | This requirement is written in passive voice and again assumes the interface is a thing. | The spacecraft shall include standardized labels, controls, and displays at the interface for ease of use. | The payload shall include standardized labels, controls, and displays at the interface for ease of use.
The electrical interface between the spacecraft and payload shall have a reliability of 0.99999. | This requirement again assumes the interface is a thing. The requirement should address each of the systems and apply to any hardware or software involved in interactions on each side of the interface boundary. | The electrical system on the spacecraft side shall maintain a reliability of 0.99999 in operations involving the payload. | The electrical system on the payload side shall maintain a reliability of 0.99999 in operations involving the spacecraft.
The SOI shall interface with …... | This requirement is ambiguous because it does not focus on a specific interaction. There are often multiple interactions; to be specific, there should be a requirement for each interaction. | The SOI shall enable data exchange with the payload's telemetry system. | The payload shall establish a secure data connection with the SOI for telemetry exchange.

## Slide 64: Steps to write Interface Requirements
Writing interface requirements is a three-step process:
Step 1: Identify the interface boundaries and interactions across those boundaries
Step 2: Define the interactions across the interface boundaries
Step 3: Write the Interface requirements.
INCOSE-TP-2021-002-01 | VERS/REV: 1.1 | May 2022

## Slide 65: System Requirements Document - Template

## Slide 66: Examples of Requirements
The <system> shall not fail.
{This is unacceptable because verification of the requirement would require infinite time.}
Acceptable:
The <system> shall have an Availability of greater than or equal to 95%.
OR
The <system> shall have a Mean Time Between Failures (MTBF) of 6 months.
INCOSE - Guide for Writing Requirements

## Slide 67: Examples of Requirements
The User_Management_System shall Open/Close the User_Account in less than 1 second.
{This is unacceptable because it is unclear as to what is meant: open, close, or both?}
Acceptable (Split into two requirements):
The User_Management_System shall Open the User_Account in less than 1 second.
The User_Management_System shall Close the User_Account in less than 1 second.
INCOSE - Guide for Writing Requirements

## Slide 68: Good Requirements or Bad Requirements?
The smart watch shall be very nice looking and easy to use.
The smart watch shall work without charging for 10 hours.
The smart watch display shall be circular with 1 inch diameter.

## Slide 69: Exercise 3.1
For your BSD ,
Transform some Stakeholder Requirements into System Requirements (following characteristics of good system requirements, and using the format “The <system> shall…”) while doing so please rectify the stakeholder requirements according to good requirement rules
  Indicate one Stakeholder Requirement in one row
  Some Stakeholder Requirements may translate into more than one System Requirement

## Slide 70
SOFTWARE REQUIREMENTS AND HW REQUIREMENTS

## Slide 71
image source: Invensity
Automotive SPICE process reference model

## Slide 72: REQUIREMENTS ANALOGY IN AUTOMOTIVE SPICE

## Slide 73: REQUIREMENTS SYS-SW TRACEBILITY AND CONSISTENCY

## Slide 74: REQUIREMENTS SYS-HW TRACEBILITY AND CONSISTENCY

## Slide 75: Needs -> STK Req ->Sys Req -> Sub-Sys Req
INCOSE-TP-2021-002-01 | VERS/REV: 1.1 | May 2022

## Slide 76
BASE PRACTICES SOFTWARE REQUIREMENTS ANALYSIS
https://polarion.code.blog/2021/04/09/swe-1-software-requirements-analysis/

## Slide 77: Architecture for Requirements Breakdown

## Slide 78: Architecture
“The fundamental organization of a system, embodied in its components, their relationships to each other and the environment, and the principles governing its design and evolution.”
- ISO/IEC/IEEE 42010

## Slide 79: Architecture
Defines…
System functionality
System boundaries relative to other systems
External interfaces with other systems
All system components
Internal interfaces between components

## Slide 80: System Hierarchy
Source : SEBOK

## Slide 81: Relationship b/w Requirements for SW intensive Systems
INCOSE-TP-2021-002-01 | VERS/REV: 1.1 | May 2022
Notes: Discussion Point : Asked the individuals to share how can they relate this diagram to their current roles.

## Slide 82: High Level Module Design: Physical Decomposition & Mapping
BSD
Sensors
Wheel Speed Sensor
Radar
Dashboard
Audio
Camera
Door sensor
BSD lamp
Speaker
Detection
Distance monitor
Object classification
Warning
visual warning
Prevent Activation
BSD
Audible warning
Interrupt Activation
speed monitoring
Door status
Standstill status
Functional
Physical
Notes: Showed as an example, but asked them to a sample breakdown of system to write requirements.

## Slide 83: Discussion
1. Create a Ref Architecture of ADAS system
2. Use the same to derive next set of HW and SW requirements

## Slide 84: Exercise 3.2
For your BSD ,
transform some Systems Requirements into Software Requirements (following characteristics of good sw requirements, and using the format “The <SW> shall…”)
  Indicate one req in one row
  Some System Requirements may translate into more than one Software Requirement

## Slide 85: Exercise 3.3
For your BSD ,
transform some Systems Requirements into Hardware Requirements (following characteristics of good hw requirements, and using the format “The <SW> shall…”)
  Indicate one req in one row
  Some System Requirements may translate into more than one HW Requirement

## Slide 86
The End